## Slide 1: Atmospheric Correction
Dan Clewley, NERC-ARF-DAN
@NERC_ARF_DAN

## Slide 2: Atmospheric Correction
Why it is needed
Some methods
Practical considerations

## Slide 3: Reflectance data
Chart: Reflectance of Grass
Chris MacLellan, NERC Field Spectroscopy Facility
This is what you would measure in the field

## Slide 4: At-sensor radiance data
This is what level 1b / 3b airborne hyperspectral data provides

## Slide 5: The path of light
Difference between surface reflectance and at-sensor radiance
  Variations in solar irradiance (time and location)
  Scattering and absorption in atmosphere
Down-welling solar irradiance
Scattering (down-welling)
Absorption (down-welling),
Surface reflectance
Scattering (up-welling),
Absorption (up-welling)
Adjacency effect.

## Slide 6: Variation in solar irradiance due to time of year and time of day
Assumes atmospheric conditions don’t change
Notes: Assume same location (Plymouth, UK) and that reflectance doesn’t change (not looking at phenology)

## Slide 7: Atmospheric Correction
Main approaches for airborne
  Image-based correction
    Normalization to a spectrally flat target (Ben-Dor et al. 1994) or an image average, e.g. dark object extraction / histogram method (Chavez 1996)
  Empirical Line Calibration
  Radiative Transfer models
Also hybrid approaches

## Slide 8
Lay out targets or use natural ones
  FSF and NERC-ARF have targets available
  Large and heavy (not suitable for all locations)
Take spectral readings at time of overpass
Empirical Line Calibration

## Slide 9
Form linear relationship for each band
Apply relationship to all pixels in flight line / flight
  Function to do this in ENVI
  We have script
Can use corrected orthogonal line to correct other lines in flight
  Applies to other correction methods (Asmat, Milton & Atkinson, 2011)
  Flow as standard for NERC-ARF data
Empirical Line Calibration
Smith & Milton 1999
Smith, G. M & Milton, E. J (1999). The use of the empirical line method to calibrate remotely sensed data to reflectance. International Journal of Remote Sensing. Volume 20, Issue 13. pages 2653-2662.
Karpouzli, E & Malthus, T (2003). The empirical line method for the atmospheric correction of IKONOS imagery. International Journal of Remote Sensing. Volume 24, Issue 5. pages 1143-1150.

## Slide 10
No differences in illumination across the image
  changes in radiance due to cloud shadowing or topography would be ignored
The effects of the atmosphere are uniform across the image.
  However, atmospheric constituents, especially water vapour, can vary greatly over short distances (Gao et al. 1991). NB: flat terrain.
The Earth’s surface consists of Lambertian reflectors
  But most surfaces have bi-directional reflectance properties (Silva 1978).
Areas of homogeneous reflectance
  Of sufficient size to account for the Point Spread Function.
Empirical Line Calibration - Assumptions
Source Gary Llewellyn, NERC-ARF

## Slide 11: Radiative Transfer (RT) models
Create a model of the atmosphere and use this to estimate absorption and scattering within the atmosphere
Examples are MODTRAN and 6S
Require a number of input parameters:
  Aerosol type
  Aerosol optical thickness
  Water vapour
Will cover in practical session
Example of ground spectra with atmosphere modelled using 6S

## Slide 12: RT modelling - Aerosol optical thickness data
Derive from image data:
  ATCOR AOT retrieval based on Dense Dark Vegetation (DDV)
Measure
  FSF sun photometer (recommended)
External data
  AERONET
Derive from image and validate
Chris MacLellan, NERC Field Spectroscopy Facility
Notes: Definition
"Aerosol Optical Thickness" is the degree to which aerosols prevent the transmission of light by absorption or scattering of light. The aerosol optical depth or optical thickness (τ) is defined as the integrated extinction coefficient over a vertical column of unit cross section. Extinction coefficient is the fractional depletion of radiance per unit path length (also called attenuation especially in reference to radar frequencies). The optical thickness along the vertical direction is also called normal optical thickness (compared to optical thickness along slant path length).
https://disc.gsfc.nasa.gov/data-holdings/PIP/aerosol_optical_thickness_or_depth.shtml

## Slide 13: RT modelling – platform and instrument characteristics
Instrument
  Range of wavelengths
  Centre wavelengths for each band
  Response function (approximate with FWHM)
  Look angle (pixel dependent)
Platform
  Height above ground (also depends on surface)
  Flight heading

## Slide 14: RT-based atmospheric correction packages
A number of software packages can perform atmospheric correction using RT models:
  FLAASH (https://www.harrisgeospatial.com/docs/FLAASH.html)
  ATCOR4 (http://www.rese.ch/products/atcor/atcor4/)

## Slide 15: Atmospheric correction using RT models
Software packages don’t always need ground data
  Should aim to collect
  Always useful to validate or use in hybrid approaches
In an idea world would parametrise model based on in situ measurements
  e.g., AOT from Sun photometer / AERONET
Needs accurate radiometric calibration
  See Aser’s Calibration talk

## Slide 16: ATCOR-4
ATCOR-4: Atmospheric & Topographic Correction
Based on MODTRAN
Algorithms to automatically derive main atmospheric parameters from the imagery
Options for
  In-flight calibration of the sensor using ground reference targets
  Interactive shadow compensation
  Simple nadir normalization (normalizing the across-track radiance gradients)
  Methods for correcting BRDF effects
Atmospherically corrected water spectra compared to in situ data
Markelin, L.; Simis, S.G.H.; Hunter, P.D.; Spyrakos, E.; Tyler, A.N.; Clewley, D.; Groom, S. Atmospheric Correction Performance of Hyperspectral Airborne Imagery over a Small Eutrophic Lake under Changing Cloud Cover. Remote Sens. 2017, 9, 2.

## Slide 17: NERC-ARF-DAN Atmospheric Correction Service
Have been developing a procedure for atmospheric correction based on ATCOR4
  Driven by requests from users
  Building on existing work at PML including satellite and work with other groups
  Focus on automation
Offer guidance or provide service
  Some users still would rather do correction themselves - have guide and scripts on GitHub (private - email for access)
  Can apply at PML for additional cost
Work in progress
  Still refining based on best practices, including field support
  Input is welcome!
Notes: Also hybrid approaches which combine RT with empirical line

## Slide 18: Best Practices - Prior to the survey
Test the instruments
  Both to check that they are working and to give you practice in using them. Ideally attend training courses such as that offered by the Field Spectroscopy Facility (FSF), this is a requirement if you borrow instruments from FSF.
Plan the survey
  Identify suitable targets before the survey day.
  Do as much planning as possible before the flight
Do a “dry run” if possible
Print off maps (+ spares)
Read scientific papers and guides on the topic
  make sure you are collecting what YOU need for YOUR study
Remember the spare batteries
  don't get out to the field only to find you have no power.
Remember to take lunch / refreshments with you - it will be a long day!
https://nerc-arf-dan.pml.ac.uk/trac/wiki/Processing/atmosphericcorrection
Notes: Also hybrid approaches which combine RT with empirical line

## Slide 19: At the survey
Do not stand between the sun and the survey point
Measure level, homogeneous targets of greater size (5 - 10 times) than the resolution of the remote sensing data
Make sure you collect more than one observation over the target to improve the measurement statistics (get as many as possible to calculate averages and standard deviations).
Try to measure near the centre of the targets rather than the edge where possible.
Always get an accurate measurement of position (use GNSS / GPS connected to the measurement instrument).
Take photographs
Measure a mixture of targets
Record the sky conditions
Measure the white reference often (every other measurement).
Go on FSF course!
https://nerc-arf-dan.pml.ac.uk/trac/wiki/Processing/atmosphericcorrection
Notes: Also hybrid approaches which combine RT with empirical line

## Slide 20: ATCOR-4 Procedure – pre processing
Apply mask to 1b data
  aplmask
Remove bands with no-data (e.g., Fenix crossover point)
  drop_nodata_bands.py / ENVI
Spectrally resample (optional – reduces noise but can remove features)
  spectral_resample.py / ENVI
Map data (optional)
  aplmap
  Also need to map sensor look angle
Convert from BIL to BSQ interleave
  convert_interleave.py / ENVI
All these steps can be run in batch / on HPC
http://github.com/pmlrsg/nerc-arf-atcor - email for access

## Slide 21: ATCOR-4 Procedure – sensor definition
Define sensor
  Specific to sensor
  Wavelengths specific to year, binning and any resampling
Define sensor response function
Resample LUT
http://github.com/pmlrsg/nerc-arf-atcor - email for access

## Slide 22: ATCOR-4 Procedure – correction
http://github.com/pmlrsg/nerc-arf-atcor - email for access
Most information in log sheet

## Slide 23: Atmospheric Correction Summary
Needs to be applied to compare data
  Different days
  Airborne vs field
  Airborne vs satellite
There are two main approaches to atmospheric correction
  Empirical Line Calibration
  Radiative Transfer models
  + Hybrids
Need to consider atmospheric correction before the flight so you can plan field data collection
  Speak to NERC-ARF and FSF for guidance / additional processing
  Not an option when using data from archive
Notes: Also hybrid approaches which combine RT with empirical line

## Slide 24: Thank you